## Slide 1
AgroSonic
Defence
IoT-Powered Smart Crop Protection System
Sri Sairam Institute • 2025
IoT Enabled
ML Powered
Mobile App
Scalable
An intelligent system integrating embedded hardware, real-time sensing, and machine learning to provide automated and adaptive protection for agricultural fields.
12 hrs
Daily Coverage
3 Types
Intruder Classes
ESP32
Core MCU
Real-Time
Notifications

## Slide 2
Project Overview
AgroSonic Defence
What is AgroSonic Defence?
IoT-enabled intelligent crop protection system designed to address agricultural intrusion by animals, birds, and humans.
Integrates PIR and ultrasonic sensors for continuous field monitoring and movement detection.
ESP32 microcontroller processes sensor data and runs a lightweight ML model to classify the type of intruder.
Activates targeted deterrents (specific sound frequencies or visual alerts) based on classification results.
Mobile app integration sends real-time notifications and allows manual farmer control.
Energy-efficient design operates 12 hours daily during high-risk periods; solar-upgradable.
Embedded Systems
ESP32 MCU with real-time sensor processing
Machine Learning
Lightweight classifier for intruder detection
Mobile Integration
Real-time alerts & manual override controls
Sustainable Design
Low-power, solar-compatible architecture

## Slide 3
Problem Statement
The Challenge
Agricultural fields face severe crop damage from animal, bird, and unauthorized human intrusions — especially at night — causing significant economic loss and farmer stress.
Night-Time Vulnerability
Intrusions peak after dark when farmers cannot monitor fields, leading to widespread crop destruction and yield loss.
Economic & Social Impact
Repeated crop damage causes financial instability for small-scale farmers and psychological stress affecting overall productivity.
Traditional Methods Fail
Manual guarding, fencing, and basic scare devices are labor-intensive, inconsistent, and ineffective over large areas.
No Intelligent Response
Existing approaches lack automation, classification ability, and real-time alerts — every intrusion is treated the same way.

## Slide 4
Existing Solutions & Gaps
Why Current Methods Fall Short
Method
What It Offers
Critical Gap
Manual Guarding
Direct human control
✗ Labor-intensive, unsustainable, risk to farmer safety at night
Physical Fencing
Permanent barrier
✗ Expensive, requires maintenance, ineffective for birds & small animals
Noise Deterrents
Low cost, easy to deploy
✗ Animals habituate over time; no classification or adaptation
Chemical Repellents
Area-wide coverage
✗ Environmental harm, inconsistent effectiveness, costly
Basic Alarm Systems
Automated alert
✗ High false alarms, no intruder classification, no targeted response
Key Gap: No existing solution provides intelligent, automated intruder classification with targeted, adaptive responses and real-time farmer notification.

## Slide 5
Proposed Solution
AgroSonic Defence System
AgroSonic Defence combines IoT sensors, ESP32 processing, machine learning classification, and mobile app integration into a fully automated, adaptive crop protection system.
01
Detect
PIR sensor detects motion
Ultrasonic sensor measures distance
Noise filtering validates data
Dual-sensor confirmation
02
Classify
Feature extraction from sensor data
ML model classifies intruder type
Bird / Animal / Human labels
Confidence level assigned
03
Respond
Type-specific sound frequency activated
LED visual alert triggered
Mobile push notification sent
Manual override available
Unlike traditional one-size-fits-all systems, AgroSonic uses different deterrent frequencies per intruder type — preventing habituation and maximizing effectiveness.

## Slide 6
Hardware & Software Architecture
Technical Stack
HARDWARE LAYER
ESP32 MCU
Central Processing Unit
Wi-Fi built-in, low power, fast processing
PIR Sensor
Motion Detection
Detects infrared heat signatures from movement
Ultrasonic Sensor
Distance Measurement
Confirms presence & estimates intruder size
Buzzer Module
Sound Deterrent
Plays frequency-specific deterrent sounds
LED Indicators
Visual Alert
Flashing alerts for visual deterrence
SOFTWARE LAYER
Arduino IDE
Development Environment
Embedded C programming for ESP32
ML Classifier
Intruder Classification
Decision tree / rule-based lightweight model
Wi-Fi Module
Cloud Communication
Sends data to mobile app via HTTP/MQTT
Mobile App
Farmer Interface
Notifications, manual control, activity logs

## Slide 7
Machine Learning Algorithm
Intelligent Intruder Classification
Model Architecture
Input Features
Motion intensity (PIR) • Distance variation (ultrasonic) • Optional thermal data
Algorithm
Decision Tree / Rule-Based Classifier — compatible with ESP32 limited RAM
Output Classes
🐦 Bird | 🐄 Animal | 👤 Human (+ confidence %)
Trigger
Classification fires on validated intrusion only — dual sensor confirmation
Adaptation
Selects specific deterrent sound per class — prevents animal habituation
Advantages
Low latency, no cloud dependency, runs on-device in real time
Classification Flow
1
Sensor Reading
PIR + Ultrasonic raw data
2
Preprocessing
Noise filter + normalization
3
Feature Extraction
Motion intensity, distance delta
4
ML Classification
Bird / Animal / Human + confidence
5
Decision & Action
Trigger targeted deterrent + alert

## Slide 8
Mobile Application & Subscription Model
User Experience & Business Strategy
Mobile App Features
Real-Time Push Alerts
Instant notification with intruder type, time, and detection zone
Manual Override
Farmer can remotely trigger stronger deterrents or disable alerts
System Dashboard
Live sensor status, battery level, Wi-Fi signal strength
Activity Log
Full history of intrusion events, response actions, and timestamps
Alert Customization
Adjust sound intensity, alert schedules, and sensitivity thresholds
Subscription Model
FREE — 6 Months
₹0
✓ Full app access
✓ Real-time notifications
✓ Basic activity logs
✓ App support
PRO — Monthly
₹199/mo
✓ All Free features
✓ Cloud data storage
✓ Advanced analytics
✓ Priority support + OTA updates

## Slide 9
Market Opportunity
Agri-Tech Market Potential
Small & Medium Farmers
Primary target — most affected by crop loss, limited access to advanced technology, price-sensitive buyers.
Agri Cooperatives
Large-scale adoption potential. Can equip thousands of member farms with a centralized subscription model.
Government & NGOs
Subsidized distribution programs for rural farmers aligned with Digital India and PM-Kisan initiatives.
140M+
Farmer Households in India
₹1.5L Cr
Annual Crop Loss Estimate
Smart Farming
Fastest Growing Agri Segment
₹199/mo
Subscription Price Point
The growing adoption of IoT and smart farming solutions, combined with digital literacy among younger farmers, creates a strong opportunity for scalable, subscription-based agri-tech deployment across rural India and beyond.

## Slide 10
Technology Stack
Core Technologies Used
Internet of Things (IoT)
Enables seamless communication between sensors, microcontroller, and the mobile application in real time.
Embedded Systems
ESP32 processes sensor data, executes control logic, and manages all hardware outputs through Embedded C on Arduino IDE.
Machine Learning
Lightweight on-device classifier differentiates between birds, animals, and humans from sensor pattern data.
Wireless Communication
Wi-Fi module on ESP32 transmits intrusion events to the cloud and pushes notifications to the farmer's smartphone.
Mobile Application
User-facing app provides real-time alerts, manual control, system status dashboard, and historical activity logs.
Cloud & Solar (Roadmap)
Future enhancement — cloud analytics for crop protection insights and solar power integration for off-grid deployment.

## Slide 11
System Flowchart
End-to-End Process Flow
A
System Start
Power ON, sensors initialize
B
PIR Detects Motion
Infrared signature detected
C
Ultrasonic Confirms
Distance + presence validated
D
Feature Extraction
Motion intensity, distance delta
E
ML Classification
Bird / Animal / Human
F
Response Selection
Type-specific sound/LED chosen
G
Deter + Notify
Buzzer + App notification sent
H
Farmer Control
Manual override if needed
Feedback Loop: If deterrent fails → Farmer manual override → System logs response → Algorithm improves over time

## Slide 12
Project Modules
Functional Architecture
01
Sensing Module
PIR + Ultrasonic sensors continuously monitor the field for motion and intrusion signals
02
Data Acquisition
Collects, filters, and normalizes raw sensor data for downstream processing
03
ML Classification
Lightweight model classifies intruder type with confidence level in real time
04
Decision Module
Determines appropriate deterrent action based on classification output
05
Actuation Module
Drives buzzer with targeted frequency and activates LED visual deterrent
06
Communication
Wi-Fi transmits event data to cloud and mobile app via MQTT/HTTP
07
User Interface
Mobile app provides push alerts, manual control, dashboards, and logs
08
Business Module
Manages subscription lifecycle, service tiers, billing, and software updates

## Slide 13
Scalability & Feasibility
Real-World Deployment Readiness
AgroSonic Defence is engineered for practical deployment — low cost, easy installation, and a modular architecture that scales from a single farm to cooperative-level coverage.
Affordability
• Low-cost, off-the-shelf components
• ESP32 < ₹500 on open market
• No specialized hardware required
• Subscription starts free for 6 months
Ease of Use
• No technical expertise needed
• Simple mobile app interface
• Plug-and-play sensor setup
• Farmer can operate independently
Scalability
• Multiple units deployable per farm
• Modular — expand coverage easily
• Cloud-ready for central management
• Supports cooperative-level adoption
Upgradability
• OTA (Over-The-Air) software updates
• Solar power add-on support
• Image recognition upgrade path
• Cloud analytics integration roadmap

## Slide 14
AgroSonic Defence
Protecting Farms. Empowering Farmers.
IoT • Machine Learning • Embedded Systems • Smart Agriculture
Sri Sairam Institute | 2025